Display Control Documentation
# Introduction
The display hardware is currently arranged in the following hierarchy:
- display_top (display_top.vhd)
  - u_display_control (display_control.vhd)
    - font ram (simple_dual_two_clocks.vhd)
Packages:
- pkg_vga_params_1280_1024_60hz.vhd
- pkg_vga_params_640_480_60hz.vhd
u_display_control takes in a pixelclk generated by a Clock Wizard IP core in display_top. It supports both 1280x1024@60Hz and 640x480@60Hz, with the output depending on which package is used in display_control.

Current issues:
All displayed char addresses are shifted by 1, so address 0 is displayed in the spot of address 1.

So when hcount_d2 =0-7, CHAR_ADDR = -1
when hcount_d2 =8-16, CHAR_ADDR = 0

CHAR_ADDR(0) and CHAR_ADDR(159) are the same character, starting at font_rom address 128

It looks like the problem is with taking an extra cycle to assert enb to read the new font row. This was leaving .
This messed up the character display, so lets revert that for now…
Our first row of image data is looking pretty screwed (need more v_count delay?, lets focus on fixing the second row of frame 2
Start by changing read_font_bit to be combinational – we don’t need to wait for ANOTHER enb to register it, as its coming straight out of the (registered) font memory.
This looks like we are now getting a proper looking character in all 4 corners of the screen. Now we just need to fix the first line of every frame.