# Wishbone Bus Notes
We will want a mixture of Wishbone classic and burst mode support.
## Wishbone Asynchronous Cycle Termination
Only available with async-read memory/registers that don’t require wait states.
## Wishbone Registered Feedback
Burst mode (Advanced Synchronous Cycle Termination) is implemented using Cycle Type Identifier (CTI) tags to allow the the address for the next transfer word to be prepped in advance (like a pipelined where the address is generated internally)
CTI_O(2:0)	Description
000	Classic Cycle (single access)
001	Constant Address burst cycle (FIFO mode)
010	Incrementing burst cycle
...	Reserved
111	End of Burst

This will improve performance for accessing synchronous-read components such as memory, if we can do burst reads into some kind of cache. It will likely prove useful for our graphics API.
We also use the Burst Type Extension (BTE_IO) tag to determine the burst behaivour
BTE_IO(1:0)	Description
00	Linear Burst (default)
01	4-beat wrapping burst
10	8-beat wrapping burst
11	16-beat wrapping burst